## Slide 1: 存储器的层次结构
存储器层次的基本概念
DRAM芯片的持续发展
主存储器组织结构
高速缓存
虚拟存储器
高速缓存的性能优化

## Slide 2: 存储器层次结构的缘起
剪刀差
Notes: Y-axis is performance
X-axis is time
Latency
Clich?
Not e that x86 didn抰 have cache on chip until 1989

## Slide 3: Introduction
Objective: programmers want unlimited amounts of memory with low latency
  CFS: Gives the allusion of a large, fast memory being presented to the processor
  Obstacle: fast memory technology is more expensive per bit than slower memory
Strategy: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest & cheapest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Action Items
  How to ensures nearly all references be found in smaller and faster memories
  Fully utilize & exploit locality!
Control
Datapath
Secondary
Storage
(HDD &
SSD)
Processor
Registers
Main
Memory
(DRAM)
Off-
Chip
Cache
(SRAM)
On-Chip
Cache
Tertiary
Storage
(Disk/
Tape)
Latency
Bandwidth
Capacity
(OCOSA)

## Slide 4: Levels of the Memory Hierarchy
Personal Mobile Device
  Smart Phone, Pad
Personal Computer
  Laptop, Desktop
Server

## Slide 5: The typical levels in the hierarchy for Desktops

## Slide 6: Processor-Memory Performance Gap “Tax”
Processor % Area %Transistors
(­cost) (­power)
Alpha 21164 37% 77%
StrongArm SA110 61% 94%
Pentium Pro 64% 88%
  2 dies per package: Proc/I$/D$ + L2$
Caches have no inherent value, only try to close performance gap
Notes: 1/3 to 2/3s of area of processor
386 had 0; successor PPro has second die!

## Slide 7: CPU Core of Zen 5

## Slide 8: The Principle of Locality
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon (e.g., loops, reuse)
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
Last 40 years, HW relied on locality for speed
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let抯 go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let抯 say you just talk to one of your friends from high school and she may say something like: 揝o did you hear so and so just won the lottery.
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)

## Slide 9: Memory Hierarchy: Terminology
Hit: data appears in some block in the upper level (example: Block X)
  Hit Rate: the fraction of memory access found in the upper level
  Hit Time: Time to access the upper level which consists of
    RAM access time + Time to determine hit/miss
Miss: data needs to be retrieve from a block in the lower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level + Time to deliver the block the processor
  Miss Time: Hit Time + Miss Penalty
Hit Time << Miss Penalty
  (500 instructions on Alpha 21264!)
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the Upper level. Then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.
+2 = 14 min. (X:54)

## Slide 10: Cache Impact to Computer Performance
1960-1985: Speed = ƒ(no. operations)
After 1990
  Pipelined Execution & Fast Clock Rate
  Out-of-Order execution
  Superscalar Instruction Issue
Now: Speed = ƒ(# of non-cached memory accesses)
What does this mean for
  Compilers? Operating Systems? Algorithms? Data Structures?

## Slide 11: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors
Aggregate peak bandwidth grows with # cores:
  Intel Core i7 can generate two references per core per clock
  Four cores and 3.2 GHz clock
    25.6 billion 64-bit data references/second +
    12.8 billion 128-bit instruction references/second = 409.6 GB/s!
  DRAM bandwidth is only 8% of this (34.1 GB/s)
  Requires:
    Multi-port, pipelined caches
    Two levels of cache per core
    Shared third-level cache on chip

## Slide 12: Main Memory Deep Background
Random Access Memory (vs. Serial Access Memory)
  Random: access time is location independent
早期计算机里用作主存的部件
  水银延迟线、示波管、磁鼓
Magnetic Core （磁心）
  “Out-of-Core”, “In-Core,” “Core Dump”?
  “Core memory”?
  Non-volatile, magnetic
  Access time 750 ns, cycle time 1500-3000 ns
半导体存储器

## Slide 13: Memory Technology
SRAM has low latency, use for cache
  Requires low power to retain bit
  Requires 6 transistors/bit
DRAM has high density, use for main mem.
  Must be re-written after being read
  Must also be periodically refreshed
    Every ~ 64 ms (roughly 5% of time)
    Each row can be refreshed simultaneously
  One transistor/bit
  Address lines are multiplexed:
    Upper half of address: row access strobe (RAS)
    Lower half of address: column access strobe (CAS)

## Slide 14: DRAM logical organization (4 Mbit)
Square root of bits per RAS/CAS
Column Decoder
Sense
Amps & I/O
Memory
Array
(2,048 x 2,048)
A0…A1
0
…
1
1
D
Q
W
ord Line
Storage
Cell
Address Buffer
Row Decoder
Bit Line
Data Out
Data In

## Slide 15: Weakness of DRAM
By it’s nature, DRAM isn’t built for speed
  Response times dependent on capacitive circuit properties which get worse as density increases
DRAM process isn’t easy to integrate into CMOS process
  DRAM is off chip
  Connectors, wires, etc. introduce slowness
  IRAM efforts looking to integrating the two
Memory Architectures are designed to minimize impact of DRAM latency
  Low Level: Memory chips
  High Level: memory system designs

## Slide 16: Memory Technology
Amdahl’s hope for a balanced computer
  Memory capacity should grow linearly with processor speed
  Unfortunately, memory capacity and speed has not kept pace with processors
Some optimizations to DRAM chips
  Multiple accesses to same row
  Synchronous DRAM
    Added clock to DRAM interface
    Burst mode with critical word first
  Wider interfaces
  Double data rate (DDR)
  Multiple banks on each DRAM device

## Slide 17: DRAM Performance Indexes
A 60 ns (tRAC) DRAM can
  perform a row access only every 110 ns (tRC)
  perform column access (tCAC) in 15 ns, but time between column accesses is at least 35 ns (tPC).
    In practice, external address delays and turning around buses make it 40 to 50 ns
  These times do not include the time to drive the addresses off the microprocessor nor the memory controller overhead!
Defined by JEDEC Solid State Technology Association
  Joint Electronic Device Engineering Council
  Rely on increasing no. of computers & memory per computer (60% market)
  Commodity, second source industry => high volume, low profit, conservative
  SIMM or DIMM is replaceable unit => computers use any generation DRAM

## Slide 18: Fast Memory Systems: DRAM specific
Page mode: All bits on the same ROW (Spatial Locality)
  Don’t need to wait for wordline to recharge
  Toggle CAS with new column address
Overlap Data output w/ CAS toggle
  Extended Data Out (EDO): 30% faster in page mode
Synchronous DRAM: Has a clock input
  Data output is in bursts w/ each element clocked
  Flavors: SDRAM, DDR (Double Data Rate)
Niche memory or main memory?
  e.g., Video RAM for frame buffers, DRAM + fast serial output

## Slide 19: RAMBUS (RDRAM)
RAMBUS: startup company; reinvent DRAM interface
  Each Chip a module vs. slice of memory, Short bus between CPU and chips
  Does own refresh; Variable amount of data returned
  1 byte / 2 ns (500 MB/s per chip); 20% increase in DRAM area
RAMBUS Bank
RDRAM Memory System

## Slide 20: DDR and GDDR Memory
DDR, Double Data Rate
  DDR2
    Lower power (2.5 V -> 1.8 V)
    Higher clock rates (266 MHz, 333 MHz, 400 MHz)
  DDR3
    1.5 V, 800 MHz3
  DDR4
    1.2 V, 1600 MHz
  DDR5
    1.1V, 3200MHz, 2 access channels
GDDR5/6 is graphics memory based on DDR3/4

## Slide 21: Capacity and access times for DDR
Access time is for a random memory word and assumes a new row must be opened. If the row is in a different bank, we assume the bank is precharged; if the row is not open, then a precharge is required, and the access time is longer. As the number of banks has increased, the ability to hide the precharge time has also increased.

## Slide 22: Clock rates, bandwidth, and names of DDR DRAMS and DIMMs in 2016
Note the numerical relationship between the columns. The third column is twice the second, and the fourth uses the number from the third column in the name of the DRAM chip. The fifth column is eight times the third column, and a rounded version of this number is used in the name of the DIMM

## Slide 23: Memory Optimizations
Reducing power in SDRAMs:
  Lower voltage
  Low power mode (ignores clock, continues to refresh)
LPDDR5
  0.5-1.05V
Graphics memory:
  Achieve 2-5 X bandwidth per DRAM vs. DDR3
    Wider interfaces (32 vs. 16 bit)
    Higher clock rate
    Possible because they are attached via soldering instead of socketed DIMM modules

## Slide 24: Memory Power Consumption
Power consumption for Micron 1.5V 2GB DDR3-1066
  In typical mode, DRAM is active 30% of the time for reads and 15% for writes

## Slide 25: Stacked/Embedded DRAMs
Stacked DRAMs in same package as processor
  High Bandwidth Memory (HBM)
3D stacking faces heat management challenges due to the xPU

## Slide 26: HBM的发展
类别 | HBM1 | HBM2 | HBM2E | HBM3 | HBM3E
带宽(GB/s) | 128 | 307 | 460 | 819 | 1225
堆叠层数 | 4 | 4/8 | 4/8 | 8/12 | 8/12
容量(GB) | 1 | 4/8 | 8/16 | 16/24 | 24/36
IO速率(Gbps) | 1 | 2.4 | 3.6 | 6.4 | 8
主要供应商与GDDR相同
  海力士、三星
  美光之前主要和Intel一起搞HMC
    最近刚加入HBM阵营

## Slide 27: Flash Memory
Type of EEPROM: Nonvolatile, can use as little as zero power
Types: NAND (denser) and NOR (faster)
  Must be erased (in blocks) before being overwritten
  Limited number of write cycles (~100,000)
Phase-Change/Memrister Memory
  Possibly 10X improvement in write performance and 2X improvement in read performance
  Intel/Micron Xpoint memory chips based on PCM
Hybrid memory system, how to manage?

## Slide 28: Main Memory Organizations
Simple:
  CPU, Cache, Bus, Memory same width (32 or 64 bits)
Wide:
  CPU/Mux 1 word; Mux/Cache, Bus, Memory N words (Alpha: 64 bits & 256 bits; UtraSPARC 512)
Interleaved:
  CPU, Cache, Bus 1 word: Memory N Modules (4 Modules); example is word interleaved

## Slide 29: Main Memory Performance
Timing model (word size is 32 bits)
  1 to send address,
  6 access time, 1 to send data
  Cache Block is 4 words
Simple Memory Performance = 4 x (1+6+1) = 32
Wide Memory Performance = 1 + 6 + 1 = 8
Interleaved Memory Performance = 1 + 6 + 4x1 = 11

## Slide 30: Independent Memory Banks
Multiple memory banks for independent accesses vs. faster sequential accesses for Multiprocessor & I/O
  CPU with Hit under n Misses, Non-blocking Cache
How many banks?
Number banks >= number clocks to access word in bank
  For sequential accesses, otherwise will return to original bank before it has next word ready
  (like in vector case)
Increasing DRAM => fewer chips => harder to have banks

## Slide 31: DRAMs per PC over Time
Minimum Memory Size
DRAM Generation
‘86 ‘89 ‘92 ‘96 ‘99 ‘02
1 Mb 4 Mb 16 Mb 64 Mb 256 Mb 1 Gb
4 MB
8 MB
16 MB
32 MB
64 MB
128 MB
256 MB
32
8
16
4
8
2
4
1
8
2
4
1
8
2

## Slide 32: Internal Organization of DRAM
Modern DRAMs are organized in banks, up to 16 for DDR4. Sending an ACT (Activate) command opens a bank and a row and loads the row into a row buffer. When the row is in the buffer, it can be transferred by successive column addresses The Precharge commend (PRE) closes the bank and row and readies it for a new access.

## Slide 33: Avoiding Bank Conflicts
Even with 128 banks, since 512 is multiple of 128, conflict on word accesses: # of banks accessed = # of banks / GCD(stride, # of banks)
int x[256][512];
for (j = 0; j < 512; j = j+1)
for (i = 0; i < 256; i = i+1)
x[i][j] = 2 * x[i][j];
SW: loop interchange or declaring array not power of 2 (“array padding”)
HW: Prime number of banks
  bank number = address % number of banks
  address within bank = address / number of words in bank (seq. interleave)
  modulo & divide per memory access with prime no. banks?
  address within bank = address % number words in bank (modulo interleave)
  bank number? easy if 2N words per bank

## Slide 34: Fast Bank Number
Chinese Remainder Theorem As long as two sets of integers ai and bi follow these rules
and that ai and aj are co-prime if i  j, then the integer x has only one solution (unambiguous mapping):
  bank number = b0, number of banks = a0 (= 3 in example)
  address within bank = b1, number of words in bank = a1 (= 8 in example)
  N word address 0 to N-1, prime no. banks, words power of 2
Seq. Interleaved Modulo Interleaved
Bank Number: 0 1 2 0 1 2 Address within Bank: 0 0 1 2 0 16 8 1 3 4 5 9 1 17 2 6 7 8 18 10 2 3 9 10 11 3 19 11 4 12 13 14 12 4 20 5 15 16 17 21 13 5 6 18 19 20 6 22 14 7 21 22 23 15 7 23

## Slide 35: Memory Dependability
Motivation:
  Failures/time proportional to number of bits!
  As DRAM cells shrink, more vulnerable to cosmic rays
Hard errors (permanent faults)
  Use spare rows inside the chip to replace defective rows
  Caused due to manufacturing, repaired during testing phase
Soft or dynamic errors (transient faults)
  Detected and fixed by error correcting codes (ECC) in runtime
Parity check works for instruction cache since read-only
  One parity bit per 8 data bits is a typical ratio
  In case multi-bit errors in longer bit strings

## Slide 36: Need for Error Correction!
Basic idea: add redundancy through more parity bits
  Simple but wasteful version:
    Keep three copies of everything, vote to find right value
    200% overhead, so not good!
  Common configuration: Random error correction
    SEC-DED (single error correct, double error detect)
    One example: 64 data bits + 8 parity bits (11% overhead)
    Papers up on reading list from last term tell you how to do these types of codes
  Really want to handle failures of physical components as well
    Organization is multiple DRAMs/DIMM, multiple DIMMs
    Want to recover from failed DRAM and failed SIMM!
    Requires more redundancy to do this
    All major vendors thinking about this in high-end machines
Chipkill: a RAID-like error recovery technique

## Slide 37: Main Memory Summary
Wider Memory
Interleaved Memory: for sequential or independent accesses
Avoiding bank conflicts: SW & HW
DRAM specific optimizations: page mode & Specialty DRAM
Need Error correction

## Slide 38: What is a cache?
Small, fast storage used to improve average access time to slow memory
Exploits spacial and temporal locality
In computer architecture, almost everything is a cache!
  Registers a cache on variables
  First-level cache a cache on second-level cache
  Second-level cache a cache on memory
  Memory a cache on disk (virtual memory)
  TLB a cache on page table
  Branch-prediction a cache on prediction information?

## Slide 39: Cache Measures
Hit rate: fraction found in that level
  So high that usually talk about Miss rate
  Miss rate fallacy: as MIPS to CPU performance, miss rate to average memory access time in memory
Average memory-access time = Hit time + Miss rate x Miss penalty (ns or clocks)
Miss penalty: time to replace a block from lower level, including time to replace in CPU
  access time: time to lower level = f(latency to lower level)
  transfer time: time to transfer block = f(BW between upper & lower levels)

## Slide 40: Simplest Cache: Direct Mapped
Memory
4 Byte Direct Mapped Cache
Memory Address
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
Cache Index
0
1
2
3
Location 0 can be occupied by data from:
  Memory location 0, 4, 8, ... etc.
  In general: any memory location whose 2 LSBs of the address are 0s
  Address<1:0> => cache index
Which one should we place in the cache?
How can we tell which one is in the cache?
Notes: Let抯 look at the simplest cache one can build. A direct mapped cache that only has 4 bytes.
In this direct mapped cache with only 4 bytes, location 0 of the cache can be occupied by data form memory location 0, 4, 8, C, ... and so on.
While location 1 of the cache can be occupied by data from memory location 1, 5, 9, ... etc.
So in general, the cache location where a memory location can map to is uniquely determined by the 2 least significant bits of the address (Cache Index).
For example here, any memory location whose two least significant bits of the address are 0s can go to cache location zero.
With so many memory locations to chose from, which one should we place in the cache?
Of course, the one we have read or write most recently because by the principle of temporal locality, the one we just touch is most likely to be the one we will need again soon.
Of all the possible memory locations that can be placed in cache Location 0, how can we tell which one is in the cache?
+2 = 22 min. (Y:02)

## Slide 41: 1 KB Direct Mapped Cache, 32B blocks
For a 2 ** N byte cache:
  The uppermost (32 - N) bits are always the Cache Tag
  The lowest M bits are the Byte Select (Block Size = 2 ** M)
Cache Index
0
1
2
3
:
Cache Data
Byte 0
0
4
31
:
Cache Tag
Example: 0x50
Ex: 0x01
0x50
Stored as part
of the cache State
Valid Bit
:
31
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
Cache Tag
Byte Select
Ex: 0x00
9
Notes: Let抯 use a specific example with realistic numbers: assume we have a 1 KB direct mapped cache with block size equals to 32 bytes.
In other words, each block associated with the cache tag will have 32 bytes in it (Row 1).
With Block Size equals to 32 bytes, the 5 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K byte, the upper 32 minus 10 bits, or 22 bits of the address will be stored as cache tag.
The rest of the address bits in the middle, that is bit 5 through 9, will be used as Cache Index to select the proper cache entry.
+2 = 30 min. (Y:10)

## Slide 42: Two-way Set Associative Cache
N-way set associative: N entries for each Cache Index
  N direct mapped caches operates in parallel (N typically 2 to 4)
  Cache Index selects a Set from the cache
  The N (two) tags in the set are compared in parallel
  Data is selected based on the tag result
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Index
Mux
0
1
Sel1
Sel0
Cache Block
Compare
Adr Tag
Compare
OR
Hit
Notes: This is called a 2-way set associative cache because there are two cache entries for each cache index. Essentially, you have two direct mapped cache works in parallel.
This is how it works: the cache index selects a set from the cache. The two tags in the set are compared in parallel with the upper bits of the memory address.
If neither tag matches the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data on the side where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 43: Disadvantage of Set Associative Cache
N-way Set Associative Cache v. Direct Mapped Cache:
  N comparators vs. 1; Extra MUX delay for the data
  Data comes AFTER Hit/Miss
Direct mapped cache, Cache Block is available BEFORE Hit/Miss:
  Possible to assume a hit and continue. Recover later if miss.
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Index
Mux
0
1
Sel1
Sel0
Cache Block
Compare
Adr Tag
Compare
OR
Hit
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associatvie cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 44: 4 Questions for Memory Hierarchy
Q1: Where can a block be placed in the upper level?
  (Block placement)
Q2: How is a block found if it is in the upper level?
  (Block identification)
Q3: Which block should be replaced on a miss?
  (Block replacement)
Q4: What happens on a write?
  (Write strategy)

## Slide 45: Q1: Where can a block be placed in the upper level?
This example cache has eight block frames and memory has 32 blocks
Block 12 placed in 8 block cache:
  Fully associative
  Direct mapped
  2-way set associative
  Set Associative Mapping => Block Number Modulo Number of Sets

## Slide 46: Q2: How is a block found if it is in the upper level?
Tag on each block
  No need to check index or block offset
Increasing associativity shrinks index, expands tag
The three portions of an address in a set associative or direct-mapped cache

## Slide 47: Q3: Which block should be replaced on a miss?
Easy for Direct Mapped
Set Associative or Fully Associative:
  Random, FIFO, LRU (Least Recently Used)
  Data cache misses per 1000 SPEC2000 instructions on Alpha
  There is little difference between LRU and random for the largest size cache, with LRU outperforming the others for smaller caches

## Slide 48: Q4: What happens on a write?
Write through The information is written to both the block in the cache and to the block in the lower-level memory.
Write back The information is written only to the block in the cache. The modified cache block is written to main memory only when it is replaced.
  Is block clean or modified (dirty)? Need dirty bit in cache Tag
Pros and Cons of each?
  WT: read misses cannot result in writes
  WB: no repeated writes to same location
WT always combined with write buffers so that don’t wait for lower level memory

## Slide 49: Write Buffer for Write Through
A Write Buffer is needed between the Cache and Memory
  Processor: writes data into the cache and the write buffer
  Memory controller: write contents of the buffer to memory
Write buffer is just a FIFO:
  Typical number of entries: 4
  Works fine if: Store frequency (w.r.t. time) << 1 / DRAM write cycle
Memory system designer’s nightmare:
  Store frequency (w.r.t. time) -> 1 / DRAM write cycle
  Write buffer saturation
Processor
Cache
Write Buffer
DRAM
Notes: You are right, memory is too slow. We really didn't writ e to the memory directly. We are writing to a write buffer.
Once the data is written into the write buffer and assuming a cache hit, the CPU is done with the write. The memory controller will then move the write buffer抯 contents to the real memory behind the scene.
The write buffer works as long as the frequency of store is not too high. Notice here, I am referring to the frequency with respect to time, not with respect to number of instructions.
Remember the DRAM cycle time we talked about last time. It sets the upper limit on how frequent you can write to the main memory.
If the store are too close together or the CPU time is so much faster than the DRAM cycle time, you can end up overflowing the write buffer and the CPU must stop and wait.
+2 = 60 min. (Y:40)

## Slide 50: Data cache organization of Opteron
The 64 KiB cache is two-way set associative with 64-byte blocks
  Size of address leaving the processor is 40 bits (physical address)
  1024 blocks = 512 blocks x 2 ways
  9-bit index selects among 512 sets
  3 bits of the block offset join the index to supply the RAM address to select the proper 8 bytes of a 64-bit word
命中时的工作步骤
  CPU给出访存地址
  用地址index部分同时访问两路
  用地址的Tag部分同时比较读出的两路Tag
  根据比较结果，两个数据块中2先1

## Slide 51: Cache performance
Miss-oriented Approach to Memory Access:
  CPIExecution includes ALU and Memory instructions
Separating out Memory component entirely
  AMAT = Average Memory Access Time
  CPIALUOps does not include memory instructions

## Slide 52: Impact on Performance
Suppose a processor executes at
  Clock Rate = 200 MHz (5 ns per cycle), Ideal (no misses) CPI = 1.1
  50% arith/logic, 30% ld/st, 20% control
Suppose that 10% of memory operations get 50 cycle miss penalty
Suppose that 1% of instructions get same miss penalty
CPI = ideal CPI + average stalls per instruction = 1.1(cycles/ins) + [ 0.30 (DataMops/ins) x 0.10 (miss/DataMop) x 50 (cycle/miss)] + [ 1 (InstMop/ins) x 0.01 (miss/InstMop) x 50 (cycle/miss)] = (1.1 + 1.5 + .5) cycle/ins = 3.1
>60% of the time the processor is stalled waiting for memory!
AMAT=(1/1.3)x[1+0.01x50]+(0.3/1.3)x[1+0.1x50]=2.54

## Slide 53: Miss per 1000 instructions
For instruction, data, and unified caches of different sizes
The percentage of instruction references is about 74%

## Slide 54: Example: Harvard Architecture
Unified vs Separate I&D (Harvard)
  16KB I&D: Inst miss rate=0.64%, Data miss rate=6.47%
  32KB unified: Aggregate miss rate=1.99%
Which is better (ignore L2 cache)?
  Assume 33% data ops  75% accesses from instructions (1.0/1.33)
  hit time=1, miss time=50
  Note that data hit has 1 stall for unified cache (only one port)
AMATHarvard=75%x(1+0.64%x50)+25%x(1+6.47%x50) = 2.05
AMATUnified=75%x(1+1.99%x50)+25%x(1+1+1.99%x50)= 2.24
Proc
I-Cache-1
Proc
Unified
Cache-1
Unified
Cache-2
D-Cache-1
Proc
Unified
Cache-2

## Slide 55: Basic Issues in VM System Design
Size of information blocks that are transferred from secondary to main storage (M)
Block of information brought into M, and M is full, then some region of M must be released to make room for the new block --> replacement policy
Which region of M is to hold the new block --> placement policy
Missing item fetched from secondary memory only on the occurrence of a fault --> demand load policy
Paging Organization
virtual and physical address space partitioned into blocks of equal size
page frames
pages
pages
reg
cache
mem
disk
frame

## Slide 56: The logical program of virtual memory
Left: contiguous virtual address space
The actual location of three of the blocks is in physical main memory and the other (D) is located on the disk

## Slide 57: Typical ranges of parameters for caches and virtual memory
Virtual memory parameters represent increases of 10–1,000,000 times over cache parameters. Usually, first-level caches contain at most 1 MiB of data, whereas physical memory contains 256 MiB to 1 TB.

## Slide 58: Virtual Memory Address Map
V = {0, 1, . . . , n - 1} virtual address space
M = {0, 1, . . . , m - 1} physical address space
MAP: V --> M U {0} address mapping function
n > m
MAP(a) = a' if data at virtual address a is present in physical
address a' and a' in M
= 0 if data at virtual address a is not present in M
Processor
Name Space V
Addr Trans
Mechanism
fault
handler
Main
Memory
Secondary
Memory
a
a
a'
0
missing item fault
physical address
OS performs
this transfer

## Slide 59: Example of how paging and segmentation divide a program
Page（页）：相同大小的块
Segment（段）：不同大小的块

## Slide 60: Paging versus Segmentation
A hybrid approach, called paged segments, shoots for the best of both worlds: segments are composed of pages, so replacing a block is easy, yet a segment may be treated as a logical unit.

## Slide 61: Paging Organization
frame 0
1
7
0
1024
7168
P.A.
Physical
Memory
1K
1K
1K
Addr
Trans
MAP
page 0
1
31
1K
1K
1K
0
1024
31744
unit of
mapping
also unit of
transfer from
virtual to
physical
memory
Virtual Memory
Address Mapping
VA
page no.
disp
10
Page Table
index
into
page
table
Page Table
Base Reg
V
Access
Rights
PA
+
table located
in physical
memory
physical
memory
address
actually, concatenation
is more likely
V.A.
Page Size通常为2的幂次

## Slide 62: Address translation & Page table lookup
It takes an extra memory access to translate VA to PA，
which makes cache access very expensive
  "innermost loop" that you want to go as fast as possible
A way to speed up translation is to use a special cache of recently used page table entries -- Translation Lookaside Buffer or TLB
  Really just a cache on the page table mappings, TLB access time comparable to cache access time (much less than main memory access time)
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data

## Slide 63: Translation Look-Aside Buffers
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
20 t
t
1/2 t
Translation
with a TLB
Just like any other cache, the TLB can be organized as fully associative, set associative, or direct mapped
TLBs are usually small, typically not more than 128 - 256 entries even on high end machines. This permits fully associative lookup on these machines. Most mid-range machines use small n-way set associative organizations.

## Slide 64: Operation of the Opteron data TLB
This TLB has 40 entries, fully associative
Memory protection
虚页号送往所有entry
V有效时，同时进行Tag比较，并检查保护状态
从Tag匹配的entry送出物理页号（40选1）
28位物理页号与12位页内偏移地址拼成40位物理地址

## Slide 65: Summary #1 / 3: The Cache Design Space
Several interacting dimensions
  cache size
  block size
  associativity
  replacement policy
  write-through vs write-back
  write allocation
The optimal choice is a compromise
  depends on access characteristics
    Workload, use (I-cache, D-cache, TLB)
  depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 66: Summary #2/3: TLB, Virtual Memory
Caches, TLBs, Virtual Memory all understood by examining how they deal with 4 questions: 1) Where can block be placed? 2) How is block found? 3) What block is repalced on miss? 4) How are writes handled?
Page tables map virtual address to physical address
TLBs are important for fast translation
TLB misses are significant in processor performance
  funny times, as most systems can’t access all of 2nd level cache without TLB misses!
Notes: Let’s do a short review of what you learned last time.
Virtual memory was originally invented as another level of memory hierarchy such that programers, faced with main memory much smaller than their programs, do not have to manage the loading and unloading portions of their program in and out of memory.
It was a controversial proposal at that time because very few programers believed software can manage the limited amount of memory resource as well as human.
This all changed as DRAM size grows exponentially in the last few decades.
Nowadays, the main function of virtual memory is to allow multiple processes to share the same main memory so we don抰 have to swap all the non-active processes to disk.
Consequently, the most important function of virtual memory these days is to provide memory protection.
The most common technique, but we like to emphasis not the only technique, to translate virtual memory address to physical memory address is to use a page table.
TLB, or translation lookaside buffer, is one of the most popular hardware techniques to reduce address translation time.
Since TLB is so effective in reducing the address translation time, what this means is that TLB misses will have a significant negative impact on processor performance.
+3 = 3 min. (X:43)

## Slide 67: Summary #3/3: Memory Hierarchy
Virtual memory was controversial at the time: can SW automatically manage 64KB across many programs?
  1000X DRAM growth removed the controversy
Today VM allows many processes to share single memory without having to swap all processes to disk
VM protection is more important than memory hierarchy
Today CPU time is a function of (ops, cache misses) vs. just f(ops): What does this mean to Compilers, Data structures, Algorithms?
Notes: Let抯 do a short review of what you learned last time.
Virtual memory was originally invented as another level of memory hierarchy such that programers, faced with main memory much smaller than their programs, do not have to manage the loading and unloading portions of their program in and out of memory.
It was a controversial proposal at that time because very few programers believed software can manage the limited amount of memory resource as well as human.
This all changed as DRAM size grows exponentially in the last few decades.
Nowadays, the main function of virtual memory is to allow multiple processes to share the same main memory so we don抰 have to swap all the non-active processes to disk.
Consequently, the most important function of virtual memory these days is to provide memory protection.
The most common technique, but we like to emphasis not the only technique, to translate virtual memory address to physical memory address is to use a page table.
TLB, or translation lookaside buffer, is one of the most popular hardware techniques to reduce address translation time.
Since TLB is so effective in reducing the address translation time, what this means is that TLB misses will have a significant negative impact on processor performance.
+3 = 3 min. (X:43)

## Slide 68: 改善Cache性能
降低不命中率
降低不命中损耗
减少命中时间

## Slide 69: Reducing Misses
Classifying Misses: 3 Cs
  Compulsory—The first access to a block is not in the cache, so the block must be brought into the cache. Also called cold start misses or first reference misses. (Misses in even an Infinite Cache)
  Capacity—If the cache cannot contain all the blocks needed during execution of a program, capacity misses will occur due to blocks being discarded and later retrieved. (Misses in Fully Associative Size X Cache)
  Conflict—If block-placement strategy is set associative or direct mapped, conflict misses (in addition to compulsory & capacity misses) will occur because a block can be discarded and later retrieved if too many blocks map to its set. Also called collision misses or interference misses. (Misses in N-way Associative, Size X Cache)
More recent, 4th “C”:
  Coherence - Misses caused by cache coherence.
Notes: Intuitive Model by Mark Hill

## Slide 70: 3Cs Absolute Miss Rate (SPEC92)
Conflict
Compulsory vanishingly
small

## Slide 71: 3Cs Relative Miss Rate
Conflict
Flaws: for fixed block size
Good: insight => invention

## Slide 72: 2:1 Cache Rule
Conflict
miss rate 1-way associative cache size X = miss rate 2-way associative cache size X/2

## Slide 73: How Can Reduce Misses?
3 Cs: Compulsory, Capacity, Conflict
In all cases, assume total cache size not changed:
What happens if:
1) Change Block Size: Which of 3Cs is obviously affected?
2) Change Associativity: Which of 3Cs is obviously affected?
3) Change Compiler: Which of 3Cs is obviously affected?
Notes: Ask which affected?
Block size
1) Compulsory
2) More subtle, will change mapping

## Slide 74: 1. Reduce Misses via Larger Block Size

## Slide 75: Actual miss rate versus block size
Note that for a 4 KiB cache, 256-byte blocks have a higher miss rate than 32-byte blocks. In this example, the cache would have to be 256 KiB in order for a 256-byte block to decrease misses

## Slide 76: Average memory access time versus block size
Block sizes of 32 and 64 bytes dominate
  The smallest average time per cache size is boldfaced

## Slide 77: 2. Reduce Misses via Higher Associativity
2:1 Cache Rule:
  Miss Rate DM cache size N ­= Miss Rate 2-way cache size N/2
Beware: Execution time is only final measure!
  Will Clock Cycle time increase?
  Hill [1988] suggested hit time for 2-way vs. 1-way: external cache +10%, internal + 2%

## Slide 78: Example: Avg. Memory Access Time vs. Miss Rate
Example: assume CCT = 1.10 for 2-way, 1.12 for 4-way, 1.14 for 8-way vs. CCT direct mapped
Cache Size Associativity
(KB) 1-way 2-way 4-way 8-way
1 2.33 2.15 2.07 2.01
2 1.98 1.86 1.76 1.68
4 1.72 1.67 1.61 1.53
8 1.46 1.48 1.47 1.43
16 1.29 1.32 1.32 1.32
32 1.20 1.24 1.25 1.27
64 1.14 1.20 1.21 1.23
128 1.10 1.17 1.18 1.20
(Red means A.M.A.T. not improved by more associativity)

## Slide 79: Average memory access time
Boldface type means larger time value than the left
  higher associativity increases average memory access time

## Slide 80: Access times generally increase as cache size and associativity increase
The data assume typical embedded SRAM technology, a single bank, and 64-byte blocks.

## Slide 81: Energy consumption per read increases as cache size and associativity increased
The large penalty for eight-way set associative caches is due to the cost of reading out eight tags and the corresponding data in parallel.

## Slide 82: 3. Reducing Misses via a “Victim Cache”
How to combine fast hit time of direct mapped yet still avoid conflict misses?
Add buffer to place data discarded from cache
Jouppi [1990]: 4-entry victim cache removed 20% to 95% of conflicts for a 4 KB direct mapped data cache
Used in Alpha, HP machines
To Next Lower Level In
Hierarchy
DATA
TAGS
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator

## Slide 83: 4. Reducing Misses via “Pseudo-Associativity”
How to combine fast hit time of Direct Mapped and have the lower conflict misses of 2-way SA cache?
Divide cache: on a miss, check other half of cache to see if there, if so have a pseudo-hit (slow hit)
Drawback: CPU pipeline is hard if hit takes 1 or 2 cycles
  Better for caches not tied directly to processor (L2)
  Used in MIPS R1000 L2 cache, similar in UltraSPARC
Hit Time
Pseudo Hit Time
Miss Penalty
Time

## Slide 84: 5. Reducing Misses by Hardware Prefetching of Instructions & Data
E.g., Instruction Prefetching
  Alpha 21064 fetches 2 blocks on a miss
  Extra block placed in “stream buffer”
  On miss check stream buffer
Works with data blocks too:
  Jouppi [1990] 1 data stream buffer got 25% misses from 4KB cache; 4 streams got 43%
  Palacharla & Kessler [1994] for scientific programs for 8 streams got 50% to 70% of misses from 2 64KB, 4-way set associative caches
Prefetching relies on having extra memory bandwidth that can be used without penalty

## Slide 85: Effects of Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
  Speedup because of hardware prefetching on Intel Pentium 4

## Slide 86: 6. Reducing Misses by Software (Compiler) Prefetching Data
Data Prefetching: Insert prefetch instructions before data is needed
  Load data into register (HP PA-RISC loads)
  Cache Prefetching: load into cache (MIPS IV, PowerPC, SPARC v. 9)
  Special prefetching instructions cannot cause faults; a form of speculative execution
Prefetching comes in two flavors:
  Binding prefetching: Requests load directly into register.
    Must be correct address and register!
  Non-Binding prefetching: Load into cache.
    Can be incorrect. Frees HW/SW to guess!
Issuing Prefetching Instructions takes time
  Is cost of prefetching issues < savings in reduced misses?
  Higher superscalar reduces difficulty of issue bandwidth

## Slide 87: 7. Reducing Misses by Compiler Optimizations
McFarling [1989] reduced caches misses by 75% on 8KB direct mapped cache, 4 byte blocks in software
Instructions: Reorder procedures in memory so as to reduce conflict misses; Profiling to look at conflicts (using tools they developed)
Data
  Merging Arrays: improve spatial locality by single array of compound elements vs. 2 arrays
  Loop Interchange: change nesting of loops to access data in stored order
  Loop Fusion: Combine 2 independent loops that have same looping and some variables overlap
  Blocking: Improve temporal locality by accessing “blocks” of data repeatedly vs. going down whole columns or rows; Requires more memory accesses but improves locality of accesses

## Slide 88: Merging Arrays Example
/* Before: 2 sequential arrays */
int val[SIZE];
int key[SIZE];
/* After: 1 array of stuctures */
struct merge {
int val;
int key;
};
struct merge merged_array[SIZE]; Reducing conflicts between val & key; improve spatial locality

## Slide 89: Loop Interchange Example
/* Before */
for (k = 0; k < 100; k = k+1)
for (j = 0; j < 100; j = j+1)
for (i = 0; i < 5000; i = i+1)
x[i][j] = 2 * x[i][j];
/* After */
for (k = 0; k < 100; k = k+1)
for (i = 0; i < 5000; i = i+1)
for (j = 0; j < 100; j = j+1)
x[i][j] = 2 * x[i][j];
Sequential accesses instead of striding through memory every 100 words; improved spatial locality

## Slide 90: Loop Fusion Example
/* Before */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
a[i][j] = 1/b[i][j] * c[i][j];
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
d[i][j] = a[i][j] + c[i][j];
/* After */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
{ a[i][j] = 1/b[i][j] * c[i][j];
d[i][j] = a[i][j] + c[i][j];}
2 misses per access to a & c vs. one miss per access; improve spatial locality

## Slide 91: Blocking Example
/* Before */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
{r = 0;
for (k = 0; k < N; k = k+1){
r = r + y[i][k]*z[k][j];};
x[i][j] = r;
};

## Slide 92: Blocking Example
Two Inner Loops:
  Read all NxN elements of z[]
  Read N elements of 1 row of y[] repeatedly
  Write N elements of 1 row of x[]
Capacity Misses a function of N & Cache Size:
  2N3 + N2 => (assuming no conflict; otherwise …)
Idea: compute on BxB submatrix that fits

## Slide 93: Blocking Example
/* After */
for (jj = 0; jj < N; jj = jj+B)
for (kk = 0; kk < N; kk = kk+B)
for (i = 0; i < N; i = i+1)
for (j = jj; j < min(jj+B-1,N); j = j+1)
{r = 0;
for (k = kk; k < min(kk+B-1,N); k = k+1) {
r = r + y[i][k]*z[k][j];};
x[i][j] = x[i][j] + r;
};
B called Blocking Factor
Capacity Misses from 2N3 + N2 to N3/B+2N2
Conflict Misses Too?

## Slide 94: Reducing Conflict Misses by Blocking
Conflict misses in caches not FA vs. Blocking size
  Lam et al [1991] a blocking factor of 24 had a fifth the misses vs. 48 despite both fit in cache

## Slide 95: Summary of Compiler Optimizations to Reduce Cache Misses (by hand)

## Slide 96: Summary: Miss Rate Reduction
3 Cs: Compulsory, Capacity, Conflict
  1. Reduce Misses via Larger Block Size
  2. Reduce Misses via Higher Associativity
  3. Reducing Misses via Victim Cache
  4. Reducing Misses via Pseudo-Associativity
  5. Reducing Misses by HW Prefetching Instr, Data
  6. Reducing Misses by SW Prefetching Data
  7. Reducing Misses by Compiler Optimizations

## Slide 97: Improving Cache Performance
1. Reduce the miss rate,
2. Reduce the miss penalty, or
3. Reduce the time to hit in the cache.

## Slide 98: Write Policy: Write-Through vs Write-Back
Write-through: all writes update cache and underlying memory/cache
  Can always discard cached data - most up-to-date data is in memory
  Cache control bit: only a valid bit
Write-back: all writes simply update cache
  Can’t just discard cached data - may have to write it back to memory
  Cache control bits: both valid and dirty bits
Other Advantages:
  Write-through: memory (or other processors) always have latest data
    Simpler management of cache
  Write-back: Better tolerance to long-latency memory?
    much lower bandwidth, since data often overwritten multiple times

## Slide 99: Write Policy 2: Write Allocate vs Non-Allocate
What happens on write-miss?
Write allocate: allocate new cache line in $
  Usually means that you have to do a “read miss” to fill in rest of the cache-line!
  Alternative: per/word valid bits
Write non-allocate (or “write-around”):
  Simply send write data through to underlying memory/cache - don’t allocate new cache line!

## Slide 100: 1. Reducing Miss Penalty: Read Priority over Write on Miss
write
buffer
CPU
in out
DRAM
(or lower mem)
Write Buffer

## Slide 101: 1. Reducing Miss Penalty: Read Priority over Write on Miss
Write-through with write buffers offer RAW conflicts with main memory reads on cache misses
  If simply wait for write buffer to empty, might increase read miss penalty (old MIPS 1000 by 50% )
  Check write buffer contents before read; if no conflicts, let the memory access continue
Write-back also want buffer to hold misplaced blocks
  Read miss replacing dirty block
  Normal: Write dirty block to memory, and then do the read
  Instead copy the dirty block to a write buffer, then do the read, and then do the write
  CPU stall less since restarts as soon as do read

## Slide 102: Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Without write merging, the words to the right would be used only for instructions that wrote multiple words at the same time
Reduces stalls due to full write buffer
No write merging
Write merging

## Slide 103: 2. Reduce Miss Penalty: Early Restart and Critical Word First
Don’t wait for full block to be loaded before restarting CPU
  Early restart — As soon as the requested word of the block arrives, send it to the CPU and let the CPU continue execution
  Critical Word First — Request the missed word first from memory and send it to the CPU as soon as it arrives; let the CPU continue execution while filling the rest of the words in the block. Also called wrapped fetch and requested word first
Generally useful only in large blocks,
Spatial locality a problem; tend to want next sequential word, so not clear if benefit by early restart
block

## Slide 104: 3.Non-blocking Caches to reduce stalls on misses
Non-blocking cache or lockup-free cache allow data cache to continue to supply cache hits during a miss
  requires special control (F/E bits on registers or out-of-order execution)
“hit under miss” reduces the effective miss penalty by working during miss vs. ignoring CPU requests
“hit under multiple miss” or “miss under miss” may further lower the effective miss penalty by overlapping multiple misses
  Significantly increases the complexity of the cache controller as there can be multiple outstanding memory accesses
  Requires multiple memory banks (otherwise cannot support bandwidth)
  Pentium Pro allows 4 outstanding memory misses

## Slide 105: Implementing Nonblocking caches
What happens on a cache miss in a blocking cache?
  Freeze pipeline in Mem stage (popular early on: SAPRC, R4000)
For nonblocking cahce, arbitration between hit and (multiple) misses
  Use Full/Empty bits in registers + MSHR queue (# of outstanding misses)
  MSHR = “Miss Status/Handler Registers”, each entry in this queue keeps track of status of outstanding memory requests to one complete memory line
    Per cache-line: keep info about memory address; For each word: register (if any) that is waiting for result; Used to “merge” multiple requests to one memory line
  New load creates MSHR entry and sets destination register to “Empty”
    Load is “released” from pipeline
  Attempt to use register before result returns causes instruction to block in decode stage.
    Limited “out-of-order” execution with respect to loads Popular with in-order superscalar architectures

## Slide 106: Performance of Nonblocking Caches
Allow hits before previous misses complete
  “Hit under miss”, “Hit under multiple miss”
  L2 must support this
Allowing one hit under miss reduces the miss penalty by 9% for integer and 12.5% for floating point Allowing a second hit improves these results to 10% and 16%
Allowing 64 results in little additional improvement

## Slide 107: 4: Add a second-level cache
L2 Equations
AMAT = Hit TimeL1 + Miss RateL1 x Miss PenaltyL1 Miss PenaltyL1 = Hit TimeL2 + Miss RateL2 x Miss PenaltyL2
AMAT = Hit TimeL1 + Miss RateL1 x (Hit TimeL2 + Miss RateL2 + Miss PenaltyL2)
Definitions:
  Local miss rate — misses in this cache divided by the total number of memory accesses to this cache (Miss rateL2)
  Global miss rate —misses in this cache divided by the total number of memory accesses generated by the CPU (Miss RateL1 x Miss RateL2)
  Global Miss Rate is what matters

## Slide 108: Comparing Local and Global Miss Rates
32 KByte 1st level cache; Increasing 2nd level cache
Global miss rate close to single level cache rate provided L2 >> L1
Don’t use local miss rate
L2 not tied to CPU clock cycle!
Cost & A.M.A.T.
Generally Fast Hit Times and fewer misses
Since hits are few, target miss reduction

## Slide 109: Relative execution time by second-level cache size
The two bars are for different clock cycles for an L2 cache hit
The reference execution time of 1.00 is for an 8192 KiB second- level cache with a 1-clock-cycle latency on a second-level hit

## Slide 110: Reducing Misses: Which apply to L2 Cache?
Reducing Miss Rate
  1. Reduce Misses via Larger Block Size
  2. Reduce Conflict Misses via Higher Associativity
  3. Reducing Conflict Misses via Victim Cache
  4. Reducing Conflict Misses via Pseudo-Associativity
  5. Reducing Misses by HW Prefetching Instr, Data
  6. Reducing Misses by SW Prefetching Data
  7. Reducing Capacity/Conf. Misses by Compiler Optimizations

## Slide 111: L2 cache block size & A.M.A.T.
32KB L1, 8 byte path to memory

## Slide 112: Reducing Miss Penalty Summary
Four techniques
  Read priority over write on miss
  Early Restart and Critical Word First on miss
  Non-blocking Caches (Hit under Miss, Miss under Miss)
  Second Level Cache
Can be applied recursively to Multilevel Caches
  Danger is that time to DRAM will grow with multiple levels in between
  First attempts at L2 caches can make things worse, since increased worst case is worse

## Slide 113: Improving Cache Performance
1. Reduce the miss rate,
2. Reduce the miss penalty, or
3. Reduce the time to hit in the cache.

## Slide 114: 1. Fast Hit times via Small and Simple Caches
Why Alpha 21164 has 8KB Instruction and 8KB data cache + 96KB second level cache?
  Small data cache and clock rate
Direct Mapped, on chip

## Slide 115: Address translation and Cache access
访问cache前，先要做地址 变换，增加一次访存
  即便用TLB，也增加了延迟
ASIDE: Why access cache with PA?
VA caches have a problem (synonym/alias problem):
  Two different virtual addresses map to same physical address => two different cache entries holding data for the same physical address!
For update: must update all cache entries with same physical address or memory becomes inconsistent
Determining this requires significant hardware, essentially an associative lookup on the physical address tags to see if you have multiple hits; or software enforced alias boundary: same lsb of VA & PA (page coloring)
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data

## Slide 116: 2. Fast hits by Avoiding Address Translation
Send virtual address to cache? Called Virtually Addressed Cache or just Virtual Cache vs. Physical Cache
  Every time process is switched logically must flush the cache; otherwise get false hits
    Cost is time to flush + Compulsory misses from empty cache
  Dealing with aliases (sometimes called synonyms); Two different virtual addresses map to same physical address
  I/O must interact with cache, so need virtual address
Solution to aliases
  HW guarantees, or SW guarantee page coloring
Solution to cache flush
  Add process identifier tag that identifies process as well as address within process: can‘t get a hit if wrong process

## Slide 117: Virtually Addressed Caches
CPU
TB
$
MEM
VA
PA
PA
Conventional
Organization
CPU
$
TB
MEM
VA
VA
PA
Virtually Addressed Cache
Translate only on miss
Synonym Problem
CPU
$
TB
MEM
VA
PA
Tags
PA
Overlap $ access
with VA translation:
requires $ index to
remain invariant
across translation
VA
Tags
L2 $

## Slide 118: 2. Fast Cache Hits by Avoiding Translation: Process ID impact
Black is uniprocess
Light Gray is multiprocess
  when flush cache
Dark Gray is multiprocess
  when use Process ID tag
Y axis: Miss Rates up to 20%
X axis: Cache size from 2 KB to 1024 KB

## Slide 119: 2. Fast Cache Hits by Avoiding Translation
Overlap the cache access with the TLB access
  High order bits of the VA are used to look in the TLB while low order bits are used as index into cache
  If index is physical part of address, can start tag access in parallel with translation so that can compare to physical tag
Limits cache to page size: what if want bigger caches and uses same trick?
  Higher associativity moves barrier to right
  Page coloring
Page Address
Page Offset
Address Tag
Index
Block Offset

## Slide 120: Overlapped Cache & TLB Access
TLB
Cache
10
2
00
4 bytes
index
1 K
page #
disp
20
12
assoc
lookup
32
PA
Hit/
Miss
PA
Data
Hit/
Miss
=
IF cache hit AND (cache tag = PA) then deliver data to CPU
ELSE IF [cache miss OR (cache tag = PA)] and TLB hit THEN
access memory with the PA from the TLB
ELSE do standard VA translation

## Slide 121: Problems With Overlapped TLB Access
Overlapped access only works as long as the address bits used to index into the cache do not change as the result of VA translation, which usually limits things to small caches, large page sizes, or high n-way set associative caches if you want a large cache
Example: suppose everything the same except that the cache is increased to 8 K bytes instead of 4 K:
Page coloring
11
2
00
virt page #
disp
20
12
cache
index
This bit is changed
by VA translation, but
is needed for cache
lookup
Solutions:
go to 8K byte page sizes;
go to 2 way set associative cache; or
SW guarantee VA[13]=PA[13]
1K
4
4
10
2 way set assoc cache

## Slide 122: The overall picture of a hypothetical memory hierarchy
Going from virtual address to L2 cache access
The page size is 16 KiB
The TLB is two-way set associative with 256 entries
The L1 cache is a direct-mapped 16 KiB, and the L2 cache is a four-way set associative with a total of 4 MiB
  Both use 64-byte blocks. The virtual address is 64 bits and the physical address is 40 bits

## Slide 123: 3. Fast Hit Times Via Pipelined Writes
Pipeline Tag Check and Update Cache as separate stages; current write tag check & previous write cache update
Only STORES in the pipeline; empty during a miss Store r2, (r1) Check r1 Add -- Sub -- Store r4, (r3) M[r1]<-r2 & check r3
In shade is Delayed Write Buffer? must be checked on reads; either complete write or read from buffer

## Slide 124: 4. Fast Writes on Misses Via Small Subblocks
If most writes are 1 word, subblock size is 1 word, & write through then always write subblock & tag immediately
  Tag match and valid bit already set: Writing the block was proper, & nothing lost by setting valid bit on again.
  Tag match and valid bit not set: The tag match means that this is the proper block; writing the data into the subblock makes it appropriate to turn the valid bit on.
  Tag mismatch: This is a miss and will modify the data portion of the block. Since write-through cache, no harm was done; memory still has an up-to-date copy of the old value. Only the tag to the address of the write and the valid bits of the other subblock need be changed because the valid bit for this subblock has already been set
Doesn’t work with write back due to last case

## Slide 125: Way Prediction
To improve hit time, predict the way to pre-set mux
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty

## Slide 126: Pipelined Caches
Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity

## Slide 127: Fast Hits by pipelining Cache Case Study: MIPS R4000
8 Stage Pipeline:
  IF–first half of fetching of instruction; PC selection happens here as well as initiation of instruction cache access.
  IS–second half of access to instruction cache.
  RF–instruction decode and register fetch, hazard checking and also instruction cache hit detection.
  EX–execution, which includes effective address calculation, ALU operation, and branch target computation and condition evaluation.
  DF–data fetch, first half of access to data cache.
  DS–second half of access to data cache.
  TC–tag check, determine whether the data cache access hit.
  WB–write back for loads and register-register operations.
What is impact on Load delay?
  Need 2 instructions between a load and its use!
Notes: Answer is 3 stages between branch and new instruction fetch and 2 stages between load and use (even though if looked at red insertions that it would be 3 for load and 2 for branch)
Reasons:
1) Load: TC just does tag check, data available after DS; thus supply the data & forward it, restarting the pipeline on a data cache miss
2) EX phase does the address calculation even though just added one phase; presumed reason is that since want fast clockc cycle don’t want to sitck RF phase with reading regisers AND testing for zero, so just moved it back on phase

## Slide 128: Case Study: MIPS R4000
IF
IS
IF
RF
IS
IF
EX
RF
IS
IF
DF
EX
RF
IS
IF
DS
DF
EX
RF
IS
IF
TC
DS
DF
EX
RF
IS
IF
WB
TC
DS
DF
EX
RF
IS
IF
TWO Cycle
Load Latency
IF
IS
IF
RF
IS
IF
EX
RF
IS
IF
DF
EX
RF
IS
IF
DS
DF
EX
RF
IS
IF
TC
DS
DF
EX
RF
IS
IF
WB
TC
DS
DF
EX
RF
IS
IF
THREE Cycle
Branch Latency
(conditions evaluated
during EX phase)
Delay slot plus two stalls
Branch likely cancels delay slot if not taken

## Slide 129: R4000 Performance
Not ideal CPI of 1:
  Load stalls (1 or 2 clock cycles)
  Branch stalls (2 cycles + unfilled slots)
  FP result stalls: RAW data hazard (latency)
  FP structural stalls: Not enough FP hardware (parallelism)
Notes: Integer programs, major delay is branch stalls
FP its structural stalls

## Slide 130: Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address
  Assuming 64 bytes per block, each of these addresses would be multiplied by 64 to get byte addressing

## Slide 131: Use HBM to Extend Hierarchy
Use HBM as off-chip L4 cache: 8GiB to 64 GiB
  High bandwidth than DDR5, but still high access latency
Where to store the TAG: use SRAM on the CPU chip
  Smaller blocks require substantial tag storage
  Larger blocks are potentially inefficient (may prefer subblock)
One approach (L-H):
  Each SDRAM row is a block index
  Each row contains set of tags and 29 data segments
  29-set associative
  Hit requires a CAS

## Slide 132: Use HBM to Extend Hierarchy
Another approach (Alloy cache):
  Mold tag and data together
  Use direct mapped mapping
Both schemes require two DRAM accesses for misses
  Two solutions:
    Use map to keep track of blocks
    Predict likely misses

## Slide 133: Average hit time latency in clock cycles
For the L-H scheme, a currently-impractical scheme using SRAM for the tags, and the alloy cache organization

## Slide 134: Use HBM to Extend Hierarchy
Performance speedup for the LH scheme, an SRAM tag scheme, and an ideal L4 (Ideal); a speedup of 1 indicates no improvement with the L4 cache, and a speedup of 2 would be achievable if L4 were perfect and took no access time.

## Slide 135: Cache Optimization Summary
Technique MR MP HT Complexity
Larger Block Size + - 0 Higher Associativity + - 1 Victim Caches + 2 Pseudo-Associative Caches + 2 HW Prefetching of Instr/Data + 2 Compiler Controlled Prefetching + 3 Compiler Reduce Misses + 0
Priority to Read Misses + 1 Subblock Placement + + 1 Early Restart & Critical Word 1st + 2 Non-Blocking Caches + 3 Second Level Caches + 2
Small & Simple Caches - + 0 Avoiding Address Translation + 2 Pipelining Writes + 1
miss rate
hit time
miss
penalty

## Slide 136: Summary
Although generally a technique helps only one factor, prefetching can reduce misses if done sufficiently early; if not, it can reduce miss penalty. + means that the technique improves the factor, − means it hurts that factor, and blank means it has no impact. The complexity measure is subjective, with 0 being the easiest and 3 being a challenge