## Slide 1: 计算机系统设计导论
计算机类型和计算模式的变迁
计算机架构和计算机产业的发展变化
技术趋势和经济规律
计算机系统的性能及其度量
成本、功耗、可靠性

## Slide 2: Classes of Computers （外形、尺寸）
Personal Mobile Device (PMD)
  e.g. start phones, tablet computers
  Emphasis on energy efficiency and real-time
Desktop Computing
  Emphasis on price-performance
Servers
  Emphasis on availability, scalability, throughput
Clusters / Warehouse Scale Computers
  Used for “Software as a Service (SaaS)”
  Emphasis on availability and price-performance
  Sub-class: Supercomputers, emphasis: floating-point performance and fast internal networks
Internet of Things/Embedded Computers
  Emphasis: price
Super Computer
Super Server
Mainframe
Department Server
Minicomputer
Workstation / Server
PC / Client
巨
大
中
小
微
数据中心
服务器集群
企业服务器
工作站、台式机
个人移动设备
物联网终端

## Slide 3: 五类计算系统的主要特征
一些销量数据（2015）
  1.6 billion PMDs (90% cell phones), 275 million desktop PCs, 15 million servers.
  The total number of embedded processors sold was nearly 19 billion.
  In total, 14.8 billion ARM-technology-based chips were shipped in 2015.
服务器和嵌入式这两类系统的价格跨度非常大
  Embedded system: from USB keys to network routers
  For servers, this range arises from the need for very large-scale multiprocessor systems for high-end transaction processing.

## Slide 4: Flynn’s Taxonomy （学术、体系结构）
Single instruction stream, single data stream (SISD)
  单指令流单数据流，传统单处理机
Single instruction stream, multiple data streams (SIMD)
  Vector architectures, Array processors （向量机、数组处理机、阵列机）
  Multimedia extensions （多媒体扩展，如MMX, 3DNow, SSE, AVX等）
  Graphics processor units （GPGPU, TPU, NPU, SIMT, etc.）
Multiple instruction streams, single data stream (MISD)
  No commercial implementation (Systolic array?)
Multiple instruction streams, multiple data streams (MIMD)
  Tightly-coupled MIMD，共享存储多处理机（多核CPU，多路服务器）
  Loosely-coupled MIMD，分布存储多计算机（MPP，服务器集群，网络计算）

## Slide 5: Computer Technology (celebrating 80 years)
Performance improvements:
  Improvements in semiconductor technology
    Feature size, clock speed
  Improvements in computer architectures
    Enabled by HLL compilers, complex O/S such as UNIX/Linux
    Lead to RISC architectures
  Together have enabled:
    Lightweight computers
    Productivity-based managed/interpreted programming languages

## Slide 6: Parallelism
并行，体系结构层面提升性能的最重要途径
Classes of parallelism in applications:
  Data-Level Parallelism (DLP)
  Task-Level Parallelism (TLP)
Classes of architectural parallelism:
  ILP: Instruction-Level Parallelism
  DLP: Vector architectures/Graphic Processor Units (GPUs)
  Thread-Level Parallelism
  Request-Level Parallelism

## Slide 7: 计算模式的变化
主机/终端
集中式计算
1950-70年代
以PC为主的
客户机/服务器
分布式计算
1980-90年代
云计算模式
云数据中心的集中
加广域网范围的分布
2000年后

## Slide 8: 食物链的例子：生物界
Big Fishes Eating Little Fishes

## Slide 9: 1988 Computer Food Chain
PC
Work-
station
Mini-
computer
Mainframe
Mini-
supercomputer
Supercomputer
Massively Parallel Processors

## Slide 10: 1998 Computer Food Chain
PC
Work-
station
Mainframe
Supercomputer
Mini-
supercomputer
Massively Parallel Processors
Mini-
computer
Now who is eating whom?
Server

## Slide 11: 现实世界中的例子：微处理器的成功
Supercomputer eaten by Workstations
  In 1996, Cray Research Inc. was acquired by SGI Corporation
  Cray Research: start from 1970’s
  SGI成立于1982年，著名产品：图形工作站、MIPS处理器
    2009年被不著名的公司并购，开发高性能计算和存储解决方案
Minicomputers eaten by PCs
  In 1998, Digital Equipment Corporation was acquired by Compaq
  DEC: start from 1960’s，著名产品：PDP 11，VAX 780
  Compaq: 康柏，1982年成立的PC公司，2002年被HP并购
  A Joke: Definitely Eaten by Compaq
“联想收购IBM”
  2005年收购PC业务，2014年收购x86服务器业务

## Slide 12: 微处理器出现后，计算平台的发展
个人计算机(PC)，不再是专业装备
  计算的普及：日常办公、休闲娱乐
智能手机(Smart Phone)
  移动性和广泛应用：饮食起居
自主驾驶汽车
  可信安全：性命交关

## Slide 13: 计算平台上CPU架构的三分天下
个人计算机(PC) x86
  计算的普及：日常办公、休闲娱乐
智能手机 ARM
  移动性和智能应用：饮食起居
自主驾驶汽车 RISC-V ?
  可信安全：性命交关

## Slide 14: 计算机架构的“分久必合”
处理器发展了好几十年，出现了许多各有特色的架构和产品，但大部分都逐渐凋零了
  Intel i860/i960, 与HP联合开发的EPIC架构IA-64（安腾）
  Motorola 的68000架构，后来跟IBM合作的PowerPC架构
  HP的PA-RISC，SUN的SPARC，DEC的Alpha，SGI的MIPS
现在桌面和云端主要采用x86架构，移动端是ARM架构
  快速收敛的原因是什么？是必然的吗，还是偶然的？
架构即“指令系统结构”：软件与硬件的接口界面
  ISA, Instruction Set Architecture

## Slide 15: 主要ISA的发展演变
1960年代，IBM 360明确了ISA的概念，为了软件的兼容
  系列机：不同性能不同成本的多种机器，使用同样的ISA
1970年代，各种ISA的试验场
  从简单的load/store结构到复杂的高级语言机，及x86
1980年代，VLSI出现，CISC/RISC之争
1990年代，超标量SuperScalar RISC设计达到巅峰
  Alpha, MIPS, Power(PC), PA-RISC, SPARC，性能都超过x86
2000年后，x86-64完胜
  CISC与RISC的融合；Intel/HP合作的EPIC未达成预期目标

## Slide 16: 关键业务领域里，RISC/EPIC的份额 也在被x86服务器逐步蚕食
Chart: 
| Government | Finance | Teleco/TEM | Utilities | Transportation | Education | Manufacturing | Internet | Resource | Health | Services | Media | Distribution | Construction
RISC/EPIC Server | 64.3487 | 188.0676 | 84.5061 | 4.3925 | 42.5167 | 2.0307 | 19.9179 | 13.4336 | 6.4138 | 0.85568 | 6.264 | 1.9199 | 0.39479 | 0.74655
4 way+ X86 Server | 730.8534 | 308.0752 | 358.9319 | 163.9692 | 80.1781 | 118.7204 | 91.0093 | 73.4588 | 74.9631 | 54.1527 | 35.9795 | 26.878 | 23.6128 | 11.1243
RISC/EPIC vs. 4 way+ X86 Server by Industry, Rolling 4 Quarters
Average growth rate: 4 way+ x86 server -7.3%, RISC/EPIC server -25.2%
关键业务领域大型主机和RISC服务器一直有优势
后来4路x86服务器大量替代了RISC/EPIC服务器
再后来，8路和4路服务器又被2路服务器替代
四路x86服务器的增长率也是负数？

## Slide 17: x86如何战胜RISC的？
x86是七〇后，RISC是八〇后
  x86长据PC市场，RISC在90年代统治服务器市场
  新世纪后，x86替代RISC，一统服务器市场
两个主要因素
  x86的持续改进
    吸收了高端RISC的实现技术，性能大幅度提高
    根据新应用的需求，不断增加新的功能指令集
  出货量大，为竞争和发展提供了动力
    PC和服务器采用相同的CPU核心架构
    大大分摊了服务器CPU的研发成本

## Slide 18: 为什么会这样？
制约高性能CPU发展的两大因素
  已有的软硬件生态系统
    存在大量标准或事实标准的接口
    如指令系统结构ISA：硬件与汇编程序员的接口
  开发新产品的成本逐渐增长
    随着工艺的发展，芯片开发的NRE日益增长
技术因素 vs. 经济因素？
  重新开发软件、开发新硬件，都有巨大成本
    软件重新开发的成本，比开发新硬件的成本还要巨大

## Slide 19: Gartner的企业软件市场分析
含企业应用软件、基础设施软件、垂直专用软件
单位：十亿美元 (US$B)
年份 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
X86软件的 市场份额 | 60% | 65% | 70% | 75% | 78% | 83% | 86% | 90% | 92% | 95%
x86软件的 营业收入 | 184 | 214 | 248 | 279 | 310 | 344 | 366 | 290 | 339 | 393
X86软件的 研发费用 | 28 | 32 | 37 | 42 | 46 | 52 | 55 | 44 | 51 | 59
参考：IDC预估2019年全球服务器市场总量为US$ 80B

## Slide 20: 90年代的超算Startups
既设计自己的CPU，又开发MPP超算系统
  nCUBE，Thinking Machines
  Kandell Square Research (KSR)
  MasPar Computer Corporation
  Meiko Scientific，……
KSR提出了名为Allcache的COMA架构
  实现了第一个cache-only memory architecture
  但其CPU只跑20MHz，同期的486已到50MHz
架构创新敌不过经济规模(律)

## Slide 21: 经济基础决定上层建筑
Architecture，既译为“建筑”，亦译为“体系结构”
技术上看，x86架构有很多问题
  采用不定长指令，指令长度从一个字节到十多个字节
  不属于通用寄存器结构，寄存器各有各的用途
  寄存器数量太少，定点的、浮点的，都少
  用FLAGS专用寄存器记录运算的进位、奇偶、零、正负等状态
微程序设计(microprogramming)技术发挥了关键作用
  Intel/AMD的不传之密，微码，可看作是一个RISC指令集
  弥补了x86架构在高性能实现方面的缺陷

## Slide 22: 示例：典型x86处理器微架构
72位的微指令
类似于RISC
前端把复杂的x86指令翻译成微指令串，即微码
后端的执行和访存部件是
纯粹的超标量RISC微架构

## Slide 23: 计算芯片产业模式的螺旋式发展
以前，系统厂商自行开发中央处理器
  CPU本身就是计算机系统的最核心内容
  VLSI时代曾有：IBM，HP，DEC，SGI，SUN，……
后来，系统厂商逐渐退出
  独立的计算芯片供应商脱颖而出：Intel，AMD，NVidia
现在，系统和平台厂商，又开始研发计算芯片了
  美国有Apple，Google，Amazon，Microsoft，等等
  中国更多：BAT都在搞，TMD跃跃欲试
    华为、联想、Oppo、小米

## Slide 24: 云服务提供商做芯片
似乎成为一个潮流
  Google TPU、AWS的ARM架构数据中心CPU
  阿里、百度也都在自研芯片
自研自用模式是行得通的
  企业盈利的基础在于其增值服务，不在硬件
    可能较容易负担起芯片研发的费用
  企业掌控全栈软硬件，生态移植的困难较小
对外提供公有云服务，还有待时日
  社会其他部分的IT系统，仍需要独立芯片商

## Slide 25: 成功和失败的再分析
在自研桌面CPU芯片方面，Apple无疑是成功的
  最早联合IBM和Motorola开发PowerPC CPU
  后来转向采用Intel CPU，近年来自研ARM架构的CPU
  表面看到的现象：Apple产品比同类产品贵很多
    不用公版的ARM CPU核，自研的CPU性能高、成本高
    配合自研的系统软件，整体达到优化的用户体验
    营销体系助力，形成“高大上”，可以卖出高价钱
云服务大厂自研自用模式是行得通的
  企业盈利的基础在于其增值服务，不在硬件
    可能较容易负担起芯片研发的费用
  企业掌控全栈软硬件，生态移植的困难较小
失败者往往只看到了“自研芯片”的表面现象
  “做芯片”如果只是为了“用芯片”，未必有价值

## Slide 26: 为什么会有这样的变化？
Performance
  Technology Advances
    CMOS VLSI dominates older technologies (TTL, ECL) in cost AND performance
  Computer architecture advances improves low-end
    RISC, superscalar, RAID, …
Price: Lower costs due to
  Simpler system development
    CMOS VLSI: smaller systems, fewer components
  Higher volumes
    CMOS VLSI : same dev. cost 10,000 vs. 10,000,000 units
  Lower margins by class of computer, due to fewer services
Function
  Rise of networking/local interconnection technology

## Slide 27: Technology Trends: Microprocessor Capacity (before 2000)
CMOS improvements:
Die size: 2X every 3 yrs
Line width: halve / 7 yrs
Alpha 21264: 15 million
Pentium Pro: 5.5 million
PowerPC 620: 6.9 million
Alpha 21164: 9.3 million
Sparc Ultra: 5.2 million
Moore’s Law
“Graduation Window”

## Slide 28: Memory Capacity before 2000 (Single Chip DRAM)
year size(Mb) cyc time
1980 0.0625 250 ns
1983 0.25 220 ns
1986 1 190 ns
1989 4 165 ns
1992 16 145 ns
1996 64 120 ns
2000 256 100 ns

## Slide 29: Technology Trends before 2000 (Summary)
Capacity Speed (latency)
Logic 2x in 3 years 2x in 3 years
DRAM 4x in 3 years 2x in 10 years
Disk 4x in 3 years 2x in 10 years

## Slide 30: Processor Performance Trends
Microprocessors
Minicomputers
Mainframes
Supercomputers
Year
0.1
1
10
100
1000
1965
1970
1975
1980
1985
1990
1995
2000

## Slide 31: Processor Performance (1.35X before, 1.55X @ 2000)
1.54X/yr

## Slide 32: Performance Trends (Summary)
Workstation performance (measured in Spec Marks) improves roughly 50% per year (2X every 18 months)
Improvement in cost performance estimated at 70% per year

## Slide 33: Growth in processor performance over 40 years
以VAX 11/780 的SPECint性能为基准，测试的是串行程序（多核系统里打开了自动并行化选项）
80年代中期以前，年平均增长22%（3.5年翻一番），主要由工艺技术驱动
86年后，增长率为52%（约2年翻一番），主要由于先进体系结构如RISC的采用
2003开始Dennard scaling失效，加上ILP有限，增长率又降至23%
2011 to 2015, 增长率降至12%, 即使用了多核，Amdahl定律的影响，并行性不够
2015后，Moore定律越来越慢，增长率降至3.5% （约20年翻一番）

## Slide 34: 典型处理器时钟频率的变化
对比上一页的性能增长
时钟频率
  主要跟工艺相关
  也跟体系结构有关
当前处理器的时钟频率
  桌面CPU最高
  服务器CPU次高
  GPU最低
跟算力性能恰恰相反
  性能vs.应用
  频率vs.功耗

## Slide 35: Trends in Technology
Integrated circuit technology (Moore’s Law)
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
DRAM capacity: 25-40%/year (slowing)
  8 Gb (2014), 16 Gb (2019), possibly no 32 Gb
Flash capacity: 50-60%/year
  8-10X cheaper/bit than DRAM
Magnetic disk capacity: recently slowed to 5%/year
  Density increases may no longer be possible, maybe increase from 7 to 9 platters
  8-10X cheaper/bit then Flash
  200-300X cheaper/bit than DRAM

## Slide 36: 部分典型计算机 部件的性能指标

## Slide 37: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns in 1971 to .011 microns in 2017
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically
Moore’s Law: number of transistors integrated in a single die
  Dennard observed in1974: voltage and current should be proportional to the linear dimensions of a transistor
  So, as the size of the transistors shrunk, and the voltage was reduced, circuits could operate at higher frequencies at the same power
  Dennard’s scaling ends at 0.13μm, stopped by threshold voltage
    Two versions of Pentium 4

## Slide 38: From ITRS to IRDSTM
ITRS: International Technology Roadmap for Semiconductors
  具备先进制程的公司：GlobalFoundaries, Intel, Samsung, and TSMC
IRDS: International Roadmap for Devices and Systems™
  一个IEEE的下属机构
Predictions of logic transistor dimensions from two editions of the ITRS report

## Slide 39: 半导体工艺与芯片设计成本
半导体工艺线的建设与开发成本
  32/28纳米的工艺开发成本是12亿美元
  22/20纳米的成本规模将增加30亿美元
  14纳米的工艺开发成本已达100亿美元？！
    台积电3nm生产线的建设成本，高达200亿美元
集成电路芯片的设计成本
  32纳米节点所需的5000万至9000万美元
  在14纳米节点后增加至1.2亿至5亿美元
芯片产品如何收回成本，实现盈利？
  量特别大，或者，毛利率比较高

## Slide 40: Computer Engineering Methodology
Technology
Trends

## Slide 41
Evaluate Existing
Systems for
Bottlenecks
Technology
Trends
Benchmarks
Computer Engineering Methodology
Notes: Where to start: existing systems bottlenecks

## Slide 42: Computer Engineering Methodology
Evaluate Existing
Systems for
Bottlenecks
Simulate New
Designs and
Organizations
Technology
Trends
Benchmarks
Workloads

## Slide 43: Computer Engineering Methodology
Evaluate Existing
Systems for
Bottlenecks
Simulate New
Designs and
Organizations
Implement Next
Generation System
Technology
Trends
Benchmarks
Workloads
Implementation
Complexity
Notes: How hard to build
Importance of simplicity (wearing a seat belt); avoiding a personal disaster
Theory vs. practice

## Slide 44: Current Trends in Architecture
Cannot continue to leverage Instruction-Level parallelism (ILP)
  Single processor performance improvement ended in 2003
New models for performance:
  Data-level parallelism (DLP)
  Thread-level parallelism (TLP)
  Request-level parallelism (RLP)
These require explicit restructuring of the application

## Slide 45: Defining Computer Architecture
Architecture (ISA), Organization, Implementation
The structure of a computer that a machine language programmer must understand to write correct (timing independent) programs for that machine (Amdahl 1964) ==> Instruction Set Architecture
“Old” view of computer architecture:
  Instruction Set Architecture (ISA) design
  i.e. decisions regarding:
    registers, memory addressing, addressing modes, instruction operands, available operations, control flow instructions, instruction encoding

## Slide 46: Instruction Set Architecture
Memory addressing
  RISC-V: byte addressed, aligned accesses faster
Addressing modes
  RISC-V: Register, immediate, displacement (base+offset)
  Other examples: autoincrement, indexed, PC-relative
Types and size of operands
  RISC-V: 8-bit, 32-bit, 64-bit

## Slide 47: Instruction Set Architecture
Operations
  RISC-V: data transfer, arithmetic, logical, control, floating point
  See Fig. 1.5 in text
Control flow instructions
  Use content of registers (RISC-V) vs. status bits (x86, ARMv7, ARMv8)
  Return address in register (RISC-V, ARMv7, ARMv8) vs. on stack (x86)
Encoding
  Fixed (RISC-V, ARMv7/v8 except compact instruction set) vs. variable length (x86)

## Slide 48: Defining Computer Architecture
“Real” computer architecture:
  Specific requirements of the target machine
  Design to maximize performance within constraints: cost, power, and availability
  Includes ISA, microarchitecture, and hardware implementation
The structure of a computer that a machine language programmer must understand to write a best programs for that machine ==> New definition of Computer Architecture
  Best: shortest execution time, lowest energy consumption, … …
Architectural Support for Programming Language and Operating Systems

## Slide 49: 体系结构：决定硬件与软件的分工
激进的结构（完全动态优化，aggressive CPU）
  硬件试图做充分的动态优化, 如COMA
  认为软件在动态分析和优化方面能力有限
  导致硬件过分复杂、功耗过高
保守的结构（静态优化，GPU、NPU等）
  硬件仅提供必需的设施, 如大量的寄存器/SRAM
  高性能能否最终达到, 完全依赖软件
  硬件简化、编程不便、性能没有保障
折衷的结构（动静态相结合的优化，普通CPU）
  硬件做一些动态的优化, 如高速缓存
  软件仍有优化的余地
  软硬件协同解决性能和编程方面的问题
应用软件
高级语言
汇编语言层
操作系统层
BIOS层次
微程序机器
数据通路控制
功能部件
门电路、触发器
晶体管和连线
指令系统结构

## Slide 50: 体系结构 设计者 面临的各种 功能需求

## Slide 51: Measurement and Evaluation
Architecture is an iterative process:
Searching the space of possible designs
At all levels of computer systems
Creativity
Good Ideas
Mediocre Ideas
Bad Ideas
Cost /
Performance
Analysis

## Slide 52: Measurement Tools
Benchmarks, Traces, Mixes
Hardware: Cost, delay, area, power estimation
Simulation (many levels)
  ISA, RT, Gate, Circuit
Queuing Theory
Rules of Thumb
Fundamental Laws & Principles

## Slide 53: Metrics of Performance
Compiler
Programming
Language
Application
Datapath
Control
Transistors
Wires
Pins
ISA
Function Units
(millions) of Instructions per second: MIPS
(millions) of (FP) operations per second: MFLOP/s
Cycles per second (clock rate)
Megabytes per second
Answers per month
Operations per second
Transactions per minute
Billions, Trillions
Transactions per second

## Slide 54: Bandwidth and Latency
Bandwidth or throughput
  Total work done in a given time
  32,000-40,000X improvement for processors
  300-1200X improvement for memory and disks
Latency or response time
  Time between start and completion of an event
  50-90X improvement for processors
  6-8X improvement for memory and disks

## Slide 55: Bandwidth and Latency
Log-log plot of bandwidth and latency milestones： latency improved 8–91 ×, while bandwidth improved about 400–32,000 ×.
Relative bandwidth improvement over time

## Slide 56: The Bottom Line: Performance (and Cost)
Time to run the task (ExTime)
  Execution time, response time, latency
Tasks per day, hour, week, sec, ns ?(Performance)
  Throughput, bandwidth
Plane
Boeing 747
BAD/Sud Concodre
Speed
610 mph
1350 mph
DC to Paris
6.5 hours
3 hours
Passengers
470
132
Throughput (pmph)
286,700
178,200
Notes: Fastest for 1 person?
Which takes less time to transport 470 passengers?

## Slide 57: The Bottom Line: Performance (and Cost)
"X is n times faster than Y" means
ExTime(Y) Performance(X)
--------- = ---------------
ExTime(X) Performance(Y)
Speed of Concorde vs. Boeing 747
Throughput of Boeing 747 vs. Concorde
Notes: 1350 / 610 = 2.2X
286,700/ 178,200 1.6X

## Slide 58: Principles of Computer Design
Take Advantage of Parallelism
  e.g. multiple processors, disks, memory banks, pipelining, multiple functional units
Principle of Locality
  Reuse of data and instructions
Focus on the Common Case
  Amdahl’s Law：改进某个部件所产生的效益，取决于该部件的使用频度

## Slide 59: Amdahl's Law
Speedup due to enhancement E:
Speedup(E) =
ExTime w/o E Performance w/ E
------------- = -------------------
ExTime w/ E Performance w/o E
Suppose that enhancement E accelerates a fraction F of the task by a factor S, and the remainder of the task is unaffected

## Slide 60: Amdahl’s Law
Floating point instructions improved to run 2X; but only 10% of actual instructions are FP
Speedupoverall
=
ExTimenew =

## Slide 61: Amdahl’s Law
Floating point instructions improved to run 2X; but only 10% of actual instructions are FP
Make the most common case Fast!
Speedupoverall
=
1
0.95
=
1.053
ExTimenew = ExTimeold x (0.9 + .1/2) = 0.95 x ExTimeold

## Slide 62: Principles of Computer Design
The Processor Performance Equation

## Slide 63: Principles of Computer Design
Different instruction types have different CPIs
  Different programs may have different CPIs too
  Suppose there are totally n instructions in the ISA

## Slide 64: Aspects of CPU Performance
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
Inst Count CPI Clock Rate
Program X
Compiler X (X)
Inst. Set. X X
Organization X X
Technology X

## Slide 65: Cycles Per Instruction
CPU time = CycleTime *  CPI * I
i = 1
n
i
i
CPI =  CPI * F where F = I
i = 1
n
i
i
i
i
Instruction Count
Instruction Frequency
Invest Resources where time is Spent!
CPI = (CPU Time * Clock Rate) / Instruction Count
  = Cycles / Instruction Count
Average Cycles per Instruction
RISC的缘起

## Slide 66: Example: Calculating CPI
Typical Mix
Base Machine (Reg / Reg)
Op Freq Cycles CPI(i) (% Time)
ALU 50% 1 .5 (33%)
Load 20% 2 .4 (27%)
Store 10% 2 .2 (13%)
Branch 20% 2 .4 (27%)
1.5

## Slide 67: Measuring Performance
Typical performance metrics:
  Response time
  Throughput
Speedup of X relative to Y
  Execution timeY / Execution timeX
Execution time
  Wall clock time: includes all system overheads
  CPU time: only computation time
Benchmarks
  Kernels (e.g. matrix multiply)
  Toy programs (e.g. sorting)
  Synthetic benchmarks (e.g. Dhrystone)
  Benchmark suites (e.g. SPEC06fp, TPC-C)

## Slide 68: SPEC: System Performance Evaluation Cooperative
First Round 1989
  10 programs yielding a single number (SPECmarks)
Second Round 1992
  SPECInt92 (6 integer programs) and SPECfp92 (14 floating point programs)
    Compiler Flags unlimited. March 93 of DEC 4000 Model 610:
  spice: unix.c:/def=(sysv,has_bcopy,bcopy(a,b,c)= memcpy(b,a,c)
  wave5: /ali=(all,dcom=nat)/ag=a/ur=4/ur=200
  nasa7: /norecu/ag=a/ur=4/ur2=200/lc=blas
Third Round 1995
  new set of programs: SPECint95 (8 integer programs) and SPECfp95 (10 floating point)
  Benchmarks useful for 3 years
  Single flag setting for all programs: SPECint_base95, SPECfp_base95

## Slide 69: SPEC: System Performance Evaluation Cooperative
Fourth Round 2000: SPEC CPU2000
  12 Integer
  14 Floating Point
  2 choices on compilation; “aggressive” (SPECint2000,SPECfp2000), “conservative” (SPECint_base2000,SPECfp_base); flags same for all programs, no more than 4 flags, same compiler for conservative, can change for aggressive
  multiple data sets so that can train compiler if trying to collect data for input to compiler to improve optimization

## Slide 70: Evolution of SPEC CPU Benchmark
10 SPEC2017 integer programs,
  5 are written in C, 4 in C++., and 1 in Fortran
13 floating-point programs,
  3 in Fortran, 2 in C++, 2 in C, and 6 in mixed C, C++, and Fortran.
6代基准共82个程序
  Gcc is the senior citizen of the group.
  Only 3 integer programs and 3 floating-point programs survived three or more generations.
Although a few are carried over from generation to generation, the version of the program changes and either the input or the size of the benchmark is often expanded to increase its running time and to avoid perturbation in measurement or domination of the execution time by some factor other than CPU time.
Integer
Floating-Point

## Slide 71: 其它SPEC基准程序

## Slide 72: How to Summarize Performance
Arithmetic mean (weighted arithmetic mean) tracks execution time: (Ti)/n or (Wi*Ti)
Harmonic mean (weighted harmonic mean) of rates (e.g., MFLOPS) tracks execution time: n/(1/Ri) or n/(Wi/Ri)
Normalized execution time is handy for scaling performance (e.g., X times faster than SPARCstation 10)
But do not take the arithmetic mean of normalized execution time, use the geometric mean: (  Tj / Nj )1/n
几何平均值的难点：一个程序算不出结果，总性能就是零！

## Slide 73: SPEC First Round
One program: 99% of time in single line of code
New front-end compiler could improve dramatically

## Slide 74: Impact of Means on SPECmark89 for IBM 550
Ratio to VAX: Time: Weighted Time:
Program Before After Before After Before After
gcc 30 29 49 51 8.91 9.22
espresso 35 34 65 67 7.64 7.86
spice 47 47 510 510 5.69 5.69
doduc 46 49 41 38 5.81 5.45
nasa7 78 144 258 140 3.43 1.86
li 34 34 183 183 7.86 7.86
eqntott 40 40 28 28 6.68 6.68
matrix300 78 730 58 6 3.43 0.37
fpppp 90 87 34 35 2.97 3.07
tomcatv 33 138 20 19 2.01 1.94
Mean 54 72 124 108 54.42 49.99
Geometric Arithmetic Weighted Arith
Ratio 1.33 Ratio 1.16 Ratio 1.09

## Slide 75: SPEC2006Cint execution times
参考机：Sun Ultra 5
评测机：AMD A10 and Intel Xeon E5-2690
当对比两台机器时，可以直接把它们的执行时间相除，再算出几何平均值
  与参考机无关

## Slide 76: Performance Evaluation
Better or worse, benchmarks shape a field
Good products created when have:
  Good benchmarks
  Good ways to summarize performance
If benchmarks/summary inadequate, then choose between improving product for real programs vs. improving product to get more sales; Sales almost always wins!
Execution time is the measure of computer performance!

## Slide 77: Gaps between Peak with Real Performance
4 multiprocessors scaled to 64 processors
The Earth Simulator and Cray X1 are vector processors. Not only did they deliver a higher fraction of peak performance, but they also had the highest peak performance and the lowest clock rates
Except for the Paratec program, the Power 4 and Itanium 2 systems delivered between 5% and 10% of their peak.

## Slide 78: 研究与工程的不同方向
2000年以后，提高单核性能已不再是学术界的研究热点
  2005年，计算所的973项目，开始把方向转到众核
但单核性能提高，仍是工程师们的努力方向

## Slide 79: 观察到的一些现象
十年之间，单核定点性能4X，单核浮点性能7X
  CPU的主频没有提高（虽然工艺在不断改进），所以性能的改进主要归功于微架构的改进
有了多核，为什么仍要改进单核？
  发挥多核性能，需要把串行程序改成并行程序
    易改，且效率不打折扣
    能改，但效率要打折扣，串行程序自动并行化的效果不尽如意
    老旧的应用、无源码的应用，基本上改不了
  大量企业关键应用，按CPU核数计算License数量
    如Oracle数据库、SAP（ERP软件）、EDA工具等
    单核性能差一倍，为了达到同样效能，购买License数量就要翻一番，成本太高

## Slide 80: 为什么对单核的改进主要在企业中进行？
原理和方法上的创新点相对少一些，不容易写Paper
  多级高速缓存
  动态多发射和乱序执行
  动态分支预测、猜测执行
稳定、精确、可预测的性能模型、方法、工具
  基于大量真实工作负荷的测量和分析（耗时）
  RTL级的快速原型装置（昂贵）
一批有经验的微架构、逻辑设计及物理设计工程师
  大学和科研机构的评价标准不同，难以支持

## Slide 81: Trends in Cost
Cost driven down by learning curve
  Yield improves with time
DRAM: price closely tracks cost
Microprocessors: price depends on volume
  10% less for each doubling of volume

## Slide 82: Wafer和die的例子
This 200 mm diameter wafer of RISC-V dies was designed by SiFive
It has two types of RISC-V dies using an older, larger processing line
An FE310 die is 2.65 mm × 2.72 mm
An SiFive test die that is 2.89 mm × 2.72 mm.
The wafer contains 1846 FE310 dies, and 1866 test dies
totaling 3712 chips

## Slide 83: Integrated Circuits Costs
Die Cost goes roughly with die area4

## Slide 84: Integrated Circuit Cost
Integrated circuit
Bose-Einstein formula:
Defects per unit area = 0.016-0.057 defects per square cm (2010)
N = process-complexity factor = 11.5-15.5 (40 nm, 2010)

## Slide 85: Photograph of an Intel Skylake microprocessor die

## Slide 86: 采用先进封装，芯片成本构成更为复杂

## Slide 87: Real World Examples
Chip Metal Line Wafer Defect Area Dies/ Yield Die Cost layers width cost /cm2 mm2 wafer
386DX 2 0.90 $900 1.0 43 360 71% $4
486DX2 3 0.80 $1200 1.0 81 181 54% $12
PowerPC 601 4 0.80 $1700 1.3 121 115 28% $53
HP PA 7100 3 0.80 $1300 1.0 196 66 27% $73
DEC Alpha 3 0.70 $1500 1.2 234 53 19% $149
SuperSPARC 3 0.70 $1700 1.6 256 48 13% $272
Pentium 3 0.80 $1500 1.5 296 40 9% $417
  From "Estimating IC Manufacturing Costs,” by Linley Gwennap, Microprocessor Report, August 2, 1993, p. 15

## Slide 88: Cost/Performance What is Relationship of Cost to Price?
Component Costs
Direct Costs (add 25% to 40%) recurring costs: labor, purchasing, scrap, warranty
Gross Margin (add 82% to 186%) nonrecurring costs: R&D, marketing, sales, equipment maintenance, rental, financing cost, pretax profits, taxes
Average Discount to get List Price (add 33% to 66%): volume discounts and/or retailer markup
Component
Cost
Direct Cost
Gross
Margin
Average
Discount
Avg. Selling Price
List Price
15% to 33%
6% to 8%
34% to 39%
25% to 40%

## Slide 89: Chip Prices (August 1993)
Assume purchase 10,000 units
Chip Area Mfg. Price Multi- Comment
        mm2 cost plier
386DX 43 $9 $31 3.4 Intense Competition
486DX2 81 $35 $245 7.0 No Competition
PowerPC 601 121 $77 $280 3.6
DEC Alpha 234 $202 $1231 6.1 Recoup R&D?
Pentium 296 $473 $965 2.0 Early in shipments

## Slide 90: Summary: Price vs. Cost

## Slide 91: 三台DELL服务器的性能和价格

## Slide 92: 三台DELL服务器的性能功耗比
An SSJ run consists of two main phases:
  The calibration phase is used to determine the maximum throughput that a system is capable of sustaining.
  Once this calibrated throughput is established, the system runs at a series of target loads. Each load runs at some percentage of the calibrated throughput.
  Ssj_ops: the number of operations finished during this measurement interval divided by the number of seconds defined for this interval, showing the throughput (workload operations per second) for this period.
Ssj_ops/watt values are on the left axis, with the three columns associated with it, and watts are on the right axis, with the three lines associated with it. The horizontal axis shows the target workload, as it varies from 100% to Active Idle. The single node R630 has the best ssj_ops/watt at each workload level, but R730 consumes the lowest power at each level.
SPECpower_ssj2008 is the first industry-standard benchmark for measuring both the performance and the power consumption of servers (SSJ: Server Side Java SSJ)

## Slide 93: Power and Energy
Problem: Get power in, get power out
Thermal Design Power (TDP)
  Characterizes sustained power consumption
  Used as target for power supply and cooling system
  Lower than peak power (1.5X higher), higher than average power consumption
Clock rate can be reduced dynamically to limit power consumption
Energy per task is often a better measurement

## Slide 94: Dynamic Energy and Power
Dynamic energy
  Transistor switch from 0 -> 1 or 1 -> 0
  ½ x Capacitive load x Voltage2
Dynamic power
  ½ x Capacitive load x Voltage2 x Frequency switched
Reducing clock rate reduces power, not energy

## Slide 95: Power
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is the limit of what can be cooled by air

## Slide 96: Techniques for Reducing Power
Do nothing well, or Clock Gating
Dynamic Voltage-Frequency Scaling (DVFS, AVFS)
  Energy savings for a server using an AMD Opteron CPU, 8 GB of DRAM, and 1 ATA disk
  At 1.8 GHz, the server can handle at most up to two-thirds of the workload without causing service- level violations
  At 1 GHz, it can safely handle only one-third of the workload
Low power state for DRAM, disks
Overclocking some cores (Turbo mode), and turning off other cores

## Slide 97: 动态功耗控制带来的性能分析难题
峰值性能的经典计算方法
  处理器峰会性能 = 每核每周期完成运算数量 核数 最高工作频率
遇到的挑战
  用哪个数据作为最高工作频率
  如果用Base，实测性能可能高于 峰值性能
  如果用Turbo？
    Max Turbo时，并不是所有核都工作
    All Core Turbo也不能长期工作
CPU Time公式中变化的时钟周期
Intel® Xeon® 6 Server Processor Specification | 
Total Cores | 32
Total Threads | 64
Max Turbo Frequency | 4.3 GHz
All Core Turbo Frequency | 4.2 GHz
Processor Base Frequency | 3.8 GHz
Cache | 144 MB
Intel® UPI Speed | 24 GT/s
Max # of UPI Links | 4
TDP | 350 W

## Slide 98: AMD Zen 5 Server Processors

## Slide 99: Static Power
Static power consumption
  25-50% of total power; to reduce: power gating
  Currentstatic x Voltage, scales with number of transistors
Comparison of the energy and die area of arithmetic operations and energy cost of accesses to SRAM and DRAM
  Area is for TSMC 45 nm technology node.

## Slide 100: Dependability
Module reliability
  Mean time to failure (MTTF)
  Mean time to repair (MTTR)
  Mean time between failures (MTBF) = MTTF + MTTR
  Availability = MTTF / MTBF
Terminology
  Reliability vs. dependability; safety vs. security
  Fault 故障, error 差错, and failure 失效
  Fault-tolerant computing, trusted computing, dependable computing
开始使用 首次失效 修复 再次失效 修复
MTTF MTTR MTBF MTTR

## Slide 101: 系统不可靠带来的影响
Figure 1.3 Costs rounded to nearest $100,000 of an unavailable system are shown by analyzing the cost of downtime (in terms of immediately lost revenue), assuming three different levels of availability, and that downtime is distributed uniformly. These data are from Landstrom (2014) and were collected and analyzed by Contingency Planning Research.

## Slide 102: Summary
Amdahl’s Law:
CPI Law:
Execution time is the real measure of computer performance!
Good products created when have:
  Good benchmarks, good ways to summarize performance
Die Cost goes roughly with die area4
Speedupoverall =
ExTimeold
ExTimenew
=
1
(1 - Fractionenhanced) + Fractionenhanced
Speedupenhanced
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle